## Slide 1: Computer Organization & Assembly language(CS-215T)
Lecture by:
Mr. Shakir Karim
Assistant Professor
DoCS&IT, SSUET
Batch 2022F

## Slide 2
Week 11
Computer Memory Types & Hierarchy,
Cache Memory
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 3: Contents To Be Covered
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Computer Memory Systems
Characteristics of Memory System
Why Computer Hierarchy?
Concept of Locality of Reference
Cache Memory and Element of Cache Design

## Slide 4: Computer Memory System
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Memory is
A logically structured – linear array of locations
Locations has addresses from 0 to maximum size a processor can address
Classification is based on distance from the processor
number of machine cycles required for access
Closer to processor, Faster the memory

## Slide 5: Characteristics Of Memory System
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 6: Memory Hierarchy
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Why Hierarchy?
To cater for the trade-off among three characteristics
How much?
i.e., Capacity?
How Fast?
i.e., Access Time?
How Expensive?
i.e., Cost?
Possible trade-off relationships hold:
Access Time Cost per bit
Capacity Cost per bit
Capacity Access Time
Dilemma exists!
Solution

## Slide 7: Memory Hierarchy
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Important Item
Locality of Reference

## Slide 8: Terms Related To Memory Hierarchy
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Hit—requested data in a given level of memory (typically, only for upper levels of memory).
Miss—requested data not in given level of memory.
Hit rate—percentage of memory accesses found in a given level of memory.
Miss rate— (1 – Hit Rate)
Hit time—time required to access the requested information in a given level of memory
Miss penalty—time required to process a miss,
  that includes replacing a block in an upper level of memory,
  plus the additional time to deliver the requested data to the processor.

## Slide 9: Locality Of Reference
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
If memory location X is accessed at time t,
(assuming no branch instructions)
there is a high probability that
memory location X + 1 will also be accessed in the near future.
This clustering of memory references into groups is an example of
Locality of Reference

## Slide 10: Locality Of Reference – Types
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Temporal locality
Recently accessed items tend to be accessed again in the near future.
Spatial locality
Accesses tend to be clustered in the address space
(for example, as in arrays or loops).
Sequential locality
Instructions tend to be accessed sequentially.

## Slide 11: Locality Of Reference – Benefit
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
a small amount of very fast memory can be used to effectively accelerate the majority of memory accesses.
REASON:
only a small amount of the entire memory space is being accessed at any given time
values in that space are being accessed repeatedly.
values from a slower memory can be copied to a smaller but faster memory that resides higher in the hierarchy.

## Slide 12: Locality Of Reference – Benefit
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
REASON:
only a small amount of the entire memory space is being accessed at any given time
values in that space are being accessed repeatedly.
values from a slower memory can be copied to a smaller but faster memory that resides higher in the hierarchy.
Results in a memory system that can store
A large amount of information in a large, low cost memory
yet provide nearly the same access speeds that would result from using very fast but expensive memory.

## Slide 13: Locality Of Reference – Example
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 14: Cache Memory
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
Cache Memory is
a relatively small, fast memory
Interposed between a larger, slower memory and
the logic that accesses the larger memory.
holds recently accessed data
designed to speed up subsequent access to the same data.
combines memory access time of
expensive, high-speed memory with
the large memory size of
less expensive, lower-speed memory.

## Slide 15: Cache Memory
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 16: Cache Memory – Organization
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 17: Cache Memory – Structure
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim
C <<<M

## Slide 18: Cache Memory – Read Operation
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 19: Cache Memory – Typical Organization
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 20: Elements Of Cache Design
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim

## Slide 21: Elements Of Cache Design
Computer Science Department & Information Technology
Sir Syed University of Engg. & Tech.
Lecture by: Mr. Shakir Karim