## Slide 1: Lecture 7
Components of Cloud Computing

## Slide 2: What is a Server?
Servers are computers that provide “services” to “clients”
They are typically designed for reliability and to service a large number of requests
Organizations typically require many physical servers to provide various services (Web, Email, Database, etc.)
Server hardware is becoming more powerful and compact

## Slide 3: Compact Servers
Organizations would like to conserve the amount of floor space dedicated to their computer infrastructure
For large-scale installations, compact servers are used. This helps with:
  Floor Space
  Manageability
  Scalability
  Power and Cooling

## Slide 4: Racks
Equipment (e.g., servers) are typically placed in racks
Equipment are designed in a modular fashion to fit into rack units (1U, 2U etc.)
A single rack can hold up to 42 1U servers
1U Server
7U Blade center

## Slide 5: Blades and Blade Enclosures
A blade server is a stripped down computer with a modular design
A blade enclosure holds multiple blade servers and provides power, interfaces and cooling for the individual blade servers

## Slide 6: What is a Data Center?
A data center is a facility used to house computer systems and associated components, such as networking and
storage systems, cooling, uninterruptable power supply, air filters…
A data center typically houses a large number of heterogeneous networked computer systems
A data center can occupy one room of a building, one or more floors, or an
entire building

## Slide 7: Data Center Components
Air conditioning
  Keep all components in the manufacturer’s recommended temperature range
Redundant Power
  UPS/Generators
  Multiple power feeds
Fire protection
Physical security
  CCTV/Access Control
Monitoring Systems
Connectivity
  Multiple ISPs/Leased Lines

## Slide 8: The Network of a Modern Data Center
CR = L3 Core Router, AR = L3 Access Router, S = L2 Switch, LB = Load Balancer,
© Carnegie MAello=n URnivaecrskityoinfQ2at0ar servers (Cisco with ~ 4,000 servers)
12
A
A
… A
A
A
… A
S
S
S
LB
S
S
S
LB
AR
AR
CR
AR
AR
CR
…
Internet
Layer 2
Layer 3

## Slide 9: Communication In Data Centers
Communication in data centers are most often based on networks running the IP protocol suite
Data centers contain a set of routers and switches that transport traffic between the servers and to the outside world
Traffic in today’s data centers:
  80% of the packets stay inside the data center
  Trend is towards even more internal communication
Typically, data centers run two kinds of applications:
  Outward facing (serving web pages to users)
  Internal computation (data mining and index computations–think of MapReduce and HPC)

## Slide 10: Communication Latency
Propagation delay in the data center is essentially 0
  Light goes a foot in a nanosecond
End to end latency comes from
  Switching latency
    10G to 10G:~ 2.5 usec (store&fwd); 2 usec (cut-thru)
  Queuing latency
    Depends on size of queues and network load
Typical times across a quiet data center: 10-20usec

## Slide 11: Elasticity and Performance
Bare data centers make it hard for applications to grow/shrink
  VLANs can be used to isolate applications from each other
    IP addresses are topologically determined by Access Routers
    Reconfiguration of IPs and VLAN trunks is painful, error- prone, slow, and often manual
    In addition, no performance isolation is provided:
      VLANs typically provide reachability isolation only
      One service sending/receiving too much traffic hurts all services sharing its subtree

## Slide 12: Power in Data Centers
Pretty good data centers have efficiency of 1.7
  0.7 Watts lost for each 1W delivered to the servers
How can we reduce power costs?
  Create servers that use less power?
    Conventional server uses 200 to 500W
    Reductions have ripple effects across entire data center
    Mostly a problem for scientists to tackle!!
  Eliminate power redundancy?
    Allow entire data centers to fail
  Reduce power usage of network gear?
    Total power consumed by switches amortizes to 10-20W per server

## Slide 13: Utilization In Data Centers
Utilization of 10% to 30% is considered “good” in data centers
Causes:
  Uneven application fit:
    Each server has CPU, memory, and disk: most applications exhaust one resource, stranding the others
  Long provisioning timescales
  Uncertainty in demand:
    Demand for a new service can spike quickly
  Risk management:
    Not having spare servers to meet application demands leads to failure

## Slide 14: What About?
Maximize useful work per dollar spent – 59% of dollars are spent on servers with very low utilization (10%)
Turn the servers into a single large resource pool and let services “breathe” : dynamically expand and contract their footprint
as needed
Two main requirements:
Enabled by Virtualization
Means for rapidly and dynamically satisfying application fluctuating resource needs
Enabled by Programming Models and Distributed File Systems
Means for servers to quickly and reliably access shared and persistent data
  Data too large to copy during provisioning process